## Slide 1
Computer Vision
PDS
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
MQTT-Message Queue Telemetry Transport
.
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/IoT_app-and-Modules
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025
Notes: https://github.com/mikeroyal/Google-Cloud-Guide

## Slide 2
MQTT - Open Connectivity for Mobile, M2M and IoT
MQTT-Message Queue Telemetry Transport
Content :
Publisher
Subscriber
Broker
Notes: https://indobot.co.id/mqtt-penting-dalam-iot/
https://bisaioti.com/protokol-mqtt/
http://www.tigli.fr/lib/exe/fetch.php?media=cours:2016_2017_mit_mqtt_lecture_2_.pdf

## Slide 3: MQTT
MQTT is described on the mqtt.org site as a machine-
to-machine (M2M) / IoT connectivity protocol.
MQTT is an Event based IoT middleware (one to many)
  publish/subscribe messaging transport protocol
  Over TCP/IP (or MQTT-S over UDP for LAN)
Its protocol is lightweight
  it can be supported by some of the smallest measuring
and monitoring devices (ex. Arduino)
  it can transmit data over far reaching networks
  It can transmit data over sometimes intermittent networks.
Event based IoT Middleware
Event pattern of communication (one to many)
Over IP (TCP)

## Slide 4: Publish / Subscribe Messaging (One to Many)
A producer publishes a message (publication) on a topic (subject)
A consumer subscribes (makes a subscription) for messages on a topic (subject)
A message server (called BROKER) matches publications to subscriptions
  If none of them match the message is discarded after modifying the topic
  If one or more matches the message is delivered to each matching consumer after
modifying the topic
Publish / Subscribe has three important characteristics:
  It decouples message senders and receivers, allowing for more flexible applications
  It can take a single message and distribute it to many consumers
  This collection of consumers can change over time, and vary based on the nature of the message.
Server

## Slide 5: MQTT Topic and Wildcards

## Slide 6: MQTT Topic : Details
A topic forms the namespace
  Is hierarchical with each “sub topic” separated by a /
  An example topic space
    A house publishes information about itself on:
      <country>/<region>/<town>/<postcode>/<house>/energyConsumption
      <country>/<region>/<town>/<postcode>/<house>/solarEnergy
      <country>/<region>/<town>/<postcode>/<house>/alarmState
      <country>/<region>/<town>/<postcode>/<house>/alarmState
    And subscribes for control commands:
      <country>/<region>/<town>/<postcode>/<house>/thermostat/setTemp
A subscriber can subscribe to an absolute topic or can use wildcards:
  Single-level wildcards “+” can appear anywhere in the topic string
  Multi-level wildcards “#” must appear at the end of the string
  Wildcards must be next to a separator
  Cannot be used wildcards when publishing
  For example
    UK/Hants/Hursley/SO212JN/1/energyConsumption
      Energy consumption for 1 house in Hursley
    UK/Hants/Hursley/+/+/energyConsumption
      Energy consumption for all houses in Hursley
    UK/Hants/Hursley/SO212JN/#
      Details of energy consumption, solar and alarm for all houses in SO212JN

## Slide 7: MQTT publish subscribe architecture
The MQTT messages are delivered asynchronously (“push”) through publish subscribe architecture.
The MQTT protocol works by exchanging a series of MQTT control packets in a defined way.
Each control packet has a specific purpose and every bit in the packet is carefully crafted to reduce the data transmitted over the network.
A MQTT topology has a MQTT server and a MQTT client.
MQTT client and server communicate through different control packets. Table below briefly describes each of these control packets.

## Slide 8: Sample of protocol use

## Slide 9: Ideal for constrained networks (low bandwidth, high latency, data limits, and fragile connections)
MQTT control packet headers are kept as small as possible.
Each MQTT control packet consist of three parts, a fixed header, variable header and payload.
Each MQTT control packet has a 2 byte Fixed header. Not all the control
packet have the variable headers and payload.
A variable header contains the packet identifier if used by the control packet.
A payload up to 256 MB could be attached in the packets.
Having a small header overhead makes this protocol appropriate for IoT by
lowering the amount of data transmitted over constrained networks.

## Slide 10: Quality of Service (QoS) for MQTT
Quality of service (QoS) levels determine how each MQTT message is
delivered and must be specified for every message sent through MQTT.
Three QoS for message delivery could be achieved using MQTT:
  QoS 0 (At most once) - where messages are delivered according to the best efforts of the operating environment. Message loss can occur.
  QoS 1 (At least once) - where messages are assured to arrive but duplicates can occur.
  QoS 2 (Exactly once) - where message are assured to arrive exactly once.
There is a simple rule when considering performance impact of QoS : “The higher the QoS, the lower the performance".

## Slide 11: Quality of Service (QoS) for MQTT

## Slide 12: MQTT Clients and APIs
You can develop an MQTT client application by programming directly to the MQTT protocol specification …… however it is more convenient to use a prebuilt client
Open Source clients available in Eclipse Paho project
  C, C++, Java, JavaScript, Lua, Python and Go
Clients for other languages are available, see mqtt.org/software
  E.g. Delphi, Erlang, .Net, Objective-C, PERL, PHP, Ruby
  Not all of the client libraries listed on mqtt.org are current. Some are at an early or experimental stage of development, whilst others are stable and mature.
Even in shell script like we are seeing in the practical course …

## Slide 13: Reference
https://www.xlsmart.co.id/bisnis/insights/article/apa-itu-protocol-mqtt/
https://thingsboard.io/docs/reference/mqtt-api/

## Slide 14
Protokol MQTT
Review::
Content :
Publish_subcribe Model
Publisher : Perangkat atau aplikasi yang mengirim data ke broker.
Subscriber : Perangkat atau aplikasi yang menerima data dari broker berdasarkan topik yang diminati.
Broker : Bertindak sebagai pusat komunikasi (Server). Tugasnya menerima pesan dari pengirim
(publisher) dan Pengirimkannya ke penerima (subscriber) yang sesua
Notes: https://indobot.co.id/mqtt-penting-dalam-iot/
https://bisaioti.com/protokol-mqtt/
http://www.tigli.fr/lib/exe/fetch.php?media=cours:2016_2017_mit_mqtt_lecture_2_.pdf

## Slide 15: Apa Itu Protokol MQTT?
MQTT (Message Queuing Telemetry Transport) adalah protokol komunikasi ringan yang dirancang untuk perangkat IoT (Internet of Things). Protokol ini menggunakan model publish-subscribe, di mana perangkat bertukar pesan melalui perantara yang disebut broker. Keunggulannya terletak pada efisiensi bandwidth, keandalan, dan kemampuannya bekerja di jaringan tidak stabil.

## Slide 16: Process>>
Setiap pesan dikirim dengan topik (misalnya: `suhu/ruang1`), yang berfungsi seperti “label” untuk mengkategorikan data.
Publisher mengirim pesan ke broker dengan menyertakan topik tertentu.
Subscriber “berlangganan” (subscribe) ke topik yang diinginkan ke broker.
Saat broker menerima pesan dari publisher, ia langsung meneruskan pesan tersebut ke semua subscriber yang berlangganan ke topik terkait. Contoh:
Sebuah sensor suhu (publisher) mengirim data ke broker dengan topik `suhu/ruang1`. Aplikasi monitoring (subscriber) yang berlangganan ke topik `suhu/ruang1` akan otomatis menerima data tersebut dari broker tanpa perlu tahu alamat sensor.
Keuntungan >>
Efisien: Pesan kecil dan minim overhead, cocok untuk jaringan lambat atau perangkat rendah daya.
Fleksibel: Komunikasi bersifat *asinkron* (publisher dan subscriber tidak perlu aktif di waktu yang sama).
Skalabel: Broker mampu mengelola ribuan perangkat sekaligus.

## Slide 17: Topic $$$
Topik adalah string yang berfungsi sebagai “alamat” atau “label” untuk mengkategorikan pesan.
Formatnya hierarkis, menggunakan garis miring (/) sebagai pemisah. Contoh: – suhu/ruang1 – sensor/kelembaban/tanah
Topik digunakan oleh broker untuk mengarahkan pesan ke subscriber yang sesuai.
Device $$$
device yang mengontrol lampu, seperti ESP32, ESP8266, atau board lainnya. Perangkat adalah (subscribe) ke topik home/office/lamp.
Saat ada pesan baru di topik tersebut, misalnya “on” atau “off”, ESP32 akan menerima pesan itu dan menyalakan atau mematikan lampu sesuai perintah.
Perangkat yang mengirim pesan ini adalah klien MQTT lain, yang bisa berupa ESP32, ESP8266, atau platform otomasi rumah yang mendukung MQTT, seperti Node-RED, Home Assistant, Domoticz, atau OpenHAB.
perangkat mengirimkan pesan “on” dan “off” ke topik home/office/lamp

## Slide 18: Payload $$$
Payload adalah isi pesan yang dikirim oleh publisher.
Formatnya fleksibel, bisa berupa teks (string), angka, JSON, XML, atau data biner, tergantung kebutuhan aplikasi.
Contoh payload: – Teks: “Suhu: 25.5°C” – JSON: {“suhu”: 25.5, “unit”: “Celsius”} – Angka: 25.5
3 level QoS dalam MQTT: QoS 0, QoS 1, dan QoS 2 $$$
QoS 0: Pesan dikirim sekali tanpa konfirmasi (fire and forget).
  Karakteristik:
    Pesan dikirim sekali saja tanpa konfirmasi penerimaan.
    Tidak ada jaminan pesan sampai ke penerima.
    Cocok untuk data yang tidak kritis atau data yang dikirim berulang (misalnya, sensor yang mengirim data secara berkala).
  Cara Kerja:
    Publisher mengirim pesan ke broker.
    Broker langsung meneruskan pesan ke subscriber tanpa menunggu konfirmasi.
    Jika pesan hilang di tengah jalan, tidak ada upaya pengiriman ulang.
  Contoh Penggunaan:
    Monitoring suhu ruangan yang tidak memerlukan keandalan tinggi.
QoS (Quality of Service) $$$#
QOS dalam MQTT adalah mekanisme yang menentukan tingkat keandalan pengiriman pesan antara publisher (pengirim), broker, dan subscriber (penerima). QoS memastikan bahwa pesan sampai ke tujuan sesuai dengan kebutuhan aplikasi, mulai dari pengiriman sederhana hingga yang lebih andal.

## Slide 19
QoS 1: Pesan dikirim minimal sekali (garansi penerimaan).
  Karakteristik:
    Pesan dijamin sampai setidaknya sekali, tetapi mungkin terjadi duplikasi.
    Ada mekanisme konfirmasi penerimaan (acknowledgment).
    Cocok untuk data yang penting tetapi toleran terhadap duplikasi.
  Cara Kerja:
    Publisher mengirim pesan ke broker dan menyimpannya sampai menerima konfirmasi (PUBACK) dari broker.
    Broker meneruskan pesan ke subscriber dan menunggu konfirmasi (PUBACK) dari subscriber.
    Jika konfirmasi tidak diterima, pesan akan dikirim ulang.
  Contoh Penggunaan*:
    Pengiriman data sensor yang penting, seperti deteksi kebakaran.
QoS 2: Pesan dikirim tepat sekali (paling andal, tetapi lambat).
  Karakteristik:
    Pesan dijamin sampai tepat sekali, tanpa duplikasi.
    Mekanisme paling andal tetapi juga paling kompleks.
    Cocok untuk data yang sangat kritis dan tidak boleh hilang atau terduplikasi.
  Cara Kerja:
    Menggunakan proses dua tahap (handshake) untuk memastikan tidak ada duplikasi:
      Publisher mengirim pesan ke broker dan menyimpannya sampai menerima konfirmasi (PUBREC).
      Broker mengirim pesan ke subscriber dan menyimpannya sampai menerima konfirmasi (PUBREC) dari subscriber.
      Setelah konfirmasi diterima, broker mengirim pesan final (PUBREL) ke publisher dan subscriber untuk menyelesaikan proses.
    Jika ada kegagalan, pesan akan dikirim ulang sesuai kebutuhan.
  Contoh Penggunaan:
    Transaksi keuangan atau sistem kontrol industri yang memerlukan keandalan tinggi.

## Slide 20: MQTT App
1. Instalasi Broker MQTT
MQTT broker yang populer adalah Mosquitto, HiveMQ, dan EMQX, yang dapat dijalankan di server lokal atau berbasis cloud untuk mendukung berbagai aplikasi seperti IoT, smart home, dan monitoring industri.
Notes: https://bisaioti.com/protokol-mqtt/

## Slide 21
Mauliate Godang